SIMULATION OF ENERGY BALANCE IN TOKAMAK t-15 UPGRADE

Yu.N. Dnestrovskij, S.E. Lysenko, S.V. Cherkasov, A.V. Danilov, A.Yu. Dnestrovskij, A.V. Sushkov

NRC «Kurchatov Institute», Institute of tokamak physics, Москва, Россия, lysenko@nfi.kiae.ru

In accordance with preliminary design, the T-15 Upgrade tokamak has the following parameters: radii R = 1.5 m, a = 0.67 m, elongation k = 1.7, triangularity =0.35, toroidal magnetic field up to Bt = 2 T, plasma current Ip =2 MA, line(averaged density (n = (2-5)× 1019 m-3. The neutral beam injection with the energy Eb = 40-80 keV and the total power QNB ( 6 MW, and ECRH with the total power QEC ( 8 MW are provided for auxiliary heating. The Canonical profiles transport model (CPTM) was used in simulations. It was verified on the MAST spherical tokamak, which has with similar parameters to T-15, and JET experiments [1]. The simplified option of the model, which solves the equations for temperatures Te and Ti, and for the current diffusion with fixed density profile, was used in calculation. The L- and H- modes are reproduced by boundary conditions for temperature and density. The deposited power profile was assessed by simple expressions [2] and calibrated by the NUBEAM code.

Simulation shows that for deuterium with Eb=80 keV and density (n =2.6 we may expect the following central temperatures:

in the Ohmic (ОН) mode: Te(0) = 2.8 keV, Ti(0) = 1.4 keV;

in the L-mode with QNB = 6 MW: Te(0) = 4.9 keV, Ti(0) = 5.4 keV;

in the H-mode with QNB = 6 MW: Te(0) = 6 keV, Ti(0) = 7.4 keV;

Figures present the central temperatures, the energy confinement time E and H–factor in the L- and H–modes as functions of the absorbed beam power.

References

Dnestrovskij Y.N. et al., Plasma Phys. Control. Fusion, 2007, v. 49, p. 1477.

Dnestrovskij Y.N., Kostomarov D.P. Numerical Simulation of Plasmas. Springer Verlag, 1986.