CALCULATION of the characteristics of ION DRIFT IN gas BY I_DRIFT CODE

R.I. Golyatina, S.A. Maiorov

A.M. Prokhorov General Physics Institute, Moscow, Russia, mayorov_sa@mail.ru

The description of the program iDrift, which calculates the characteristics of the ion drift in a gas at a constant and uniform electric field. The gas may be your own (the same kind that the ion), and the improper mixture of gases of different concentrations. We consider a swarm of ions, each of which starts from the initial point and accelerated by a constant and uniform electric field. At some point of time, there is a ion-atom collision, the probability of such an event is played out from the known collision cross sections of different types.

Considered a collision with resonance charge transfer, polarization interaction and repulsion due to the interaction of the electron shells. Model of ion-atom collisions, implemented by Monte Carlo, can properly take into account the energy balance of the ions as they drift [1].

This formulation of the problem allows us to calculate all the kinetic transport coefficients are needed to simulate a spatially inhomogeneous plasma and non-stationary processes in it:

- Coefficient of ion mobility and diffusion along and across the field,

- Distribution function of the velocity in the direction along and across the field,

- Angular and energy distribution of ions bombarding the surface.

The last two characteristics determine, for example, the efficiency and the quality of the ion etching of semiconductor wafers in a plasma chemical reactors.

This program is used mainly for modeling of transport processes in dusty plasma, where the ion-atom collisions, despite their rarity, may have a decisive influence on the characteristics of the dust subsystem in plasma [2, 3].

In addition to the experiments in normal conditions considered as experiments at cryogenic temperatures, the gas [4], and mixtures of the noble gases [5, 6]. Completed program iDrift calculations [7] revealed a deep analogy between the discharge and the discharge cryogenically in a mixture of light and heavy gas, led to significant findings for the theory of the applicability of the widely used BGK approximation [8].

The study was supported by The Ministry of education and science of Russia, project 8392.

References

Maiorov S.A Physics of Plasmas, 2009, Т. 35, №9, с. 869-880.

Maiorov S.A., Physics of Plasmas, 2005, Т. 31, №8, с.749.

Maiorov S.A., Physics of Plasmas, 2006, Т. 32, №9, с. 802-815.

Antipov S.N., Asinovski A.I., Kirillin А.V., Maiorov S.A., Markovets V.V., Petrov О.F., Fortov V.Е., JETP, 2008, 133, issue 4, 948.

Maiorov S.A., Ramazanov T.S., Dzhumagulova K.N., Jumabekov A.N.  and Dosbolaev A.N., Physics of Plasmas, 2008, 15, 093701.

Antipov S.N., Vasilev М.М., Maiorov S.A., Petrov О.F., Fortov V.Е., JETP, 2011, 139, issue 3, 554.

Golyatina R.I., Maiorov S.A., Brief reports on physics LPI, 2012,  № 9, 30.

Maiorov S.A., Citovich V.N., Brief reports on physics LPI, 2012,  № 3, 14.