Simulation of density and temperature profiles from THE MAST tokamak

A.V. Danilov, Yu.N. Dnestrovskij, A.Yu. Dnestrovskij, S.E. Lysenko, S.V. Cherkasov

RRC ‘Kurchatov Institute’, Moscow, Russia, e-mail: danilov@nfi.kiae.ru

The spherical tokamak MAST shots simulation was performed by means of the canonical profiles transport model (CPTM), presented in the report [1]. A number of L- and H-mode pulses was under consideration. The model has proved to describe correctly the common features of the H-mode in MAST: relatively low temperature pedestal (100 ( 200 eV), high density pedestal and flat or even “hole-like” density profile in the plasma core. The relation of these peculiarities to transport coefficients and pinch velocity profiles is presented.

The work is supported by Rosatom, Agreement UKAEA 3000080910, and Grants NSh-2264.2006.2 and NWO-RFBR 047.016.015.

References

- Dnestrovskij Yu.N., Danilov A.V., Dnestrovskij A.Yu., Kirneva N.A., Lysenko S.E. and Cherkasov S.V. Proc. 35-th Zvenigorod International Conference on Plasma Physics and Controlled Fusion, Moscow 2008.