On Negligible role of neutral flux variations on temperature evolution in core region of JET and JT-60U tokamaks at Global L-H and H-L transitions

S.V. Neudatchin, T. Takizuka*

Tokamak Physics Institute, RRC "Kurchatov Institute", 123182, Moscow, Russia,
     e-mail: neudathin@nfi.kiae.ru
*JAEA,  Naka Fusion Res. Est. Naka-machi, Naka-gun, Ibaraki-ken 311-0193 Japan

Global L-H and H-L transitions were observed in JET tokamak [1-2] initially. The temperature in 90% of plasma volume started to rise (decrease) simultaneously with fast drop (increase) of Dα. This data was interpreted as abrupt non-local reduction (increase) of heat (electron and electron) heat diffusivities coefficients [1-2]. The profiles of jumps of heat diffusivities coefficients were evaluated. Similar global transitions were found later in various regimes of JT-60U tokamak [3-4] (with normal and reversed magnetic shear, with and without internal transport barriers). The authors of paper [5] presented results of transport code calculations with alternative explanation of the temperature rise in 90% of plasma volume of JET at the time of L-H transition. Neutral influx from the wall has significant part of neutrals with high energy. Correspondingly, calculated neutrals penetrate up to plasma centre. The decrease of neutral flux creates non-local temperature rise at L-H transition [5]. Similar calculations were already done earlier [2] and calculated data was not consistent with particular shot analysed.

In the present report, we analyse applicability of hypothesis [5] to the variety of JET and JT-60U shots [1-4] with various density and plasma parameters. Some important detail of JT-60U data are shown. New formulae allow us to analyse sequences of hypothesis [5] to each experiment separately. Finally, hypothesis [5] is found to be in systematic contradiction with experiments.

References

Neudatchin S.V., Cordey J.G., Miur D. 20th EPS Conf. on Plasma Ph. Lisboa, 1993, v.I, p. 83

Cordey J.G., Miur D., Neudatchin S.V., et. al., Nucl. Fusion 1995 35 101

Neudatchin S.V., Takizuka T. et.al., Japan J. Appl. Phys. 1996 35 3595

Neudatchin S.V., Takizuka T. et.al., Plasma Phys. Control. Fusion 2002 42 A383

Leonov V.M., Zhogolev V.E. 22nd IAEA Fusion Energy Conf. 2008 Geneva TH/P8-25